## Slide 1
Recognition of Underground Target Material Based on Average Phase Difference and Radial Basis Function Neural Network
Kunzhe Li, Shufang Liu, Xiaowei Shi, Yuan Xue, Dalin Zhang
School of Electronic Engineering, Xidian University, Xi’an, 710071, China
Corresponding author. E-mails : lkzfig@163.com
ABSTRACT
Recognition of the material of underground targets is always an important part of GPR (Ground Penetrating Radar) applications. According to target return time, truncating the data to remove the direct waves, and then select the typical data of the different materials target echoes. By comparing the phase of different targets with that of no target, the average phase difference is obtained. And the average phase difference is used as the input of the RBF (Radial Basis Function) neural network to realize the classification and recognition of underground target materials. Simulation result shows that this method can realize the identification and classification of common materials, such as metals, water and hole.
RBF NEURAL NETWORK
CONCLUSION
This paper proposes a method for GPR underground target material recognition based on the combination of RBF neural network and average phase difference. The radar echo signal is preprocessed to calculate the average phase difference between the target signal and the reference signal.
GPRMAX2.0 is used to simulate the model that is shown in Fig. 3. The excitation signal is the Ricker wavelet. The center frequency is 100MHz, and the background medium is concrete with a relative dielectric constant of 5. The target in the model is a sphere with a radius of 2.5m and buried depth of 10m. The sphere is filled with water (dielectric constant of 81), metal and hollow respectively. In order to contrast, a no target signal is selected as the reference signal.The simulation results are shown in Fig. 2.
Fig.2.(a) Simulation model.
Fig. 2.(c) RBF neural network test results.
In the RBF neural network, the radial basis function is used as the "base" of the hidden unit to form the hidden layer space so that the input vector can be directly mapped to the hidden space. The hidden layer can map the vector from the low dimension to the high dimension, which makes the linearly inseparable situation linearly separable.
The RBF neural network is composed of three parts, the input layer, the hidden layer and the output layer. For neural networks, the most important thing is to determine hidden layer neurons. In this paper, since the number of categories is certain, k-means clustering can be used to get the hidden layer of neurons. When the neurons of the hidden layer are determined, the output of the hidden layer neurons is known, and the connection weights of the neural network can be calculated by solving the linear equations.
Fig.1. The schematic diagram of the RBF neural network.
After obtaining the typical echo data, we can calculate phase spectrum of each target of different materials. The echo signal data when there is no target is selected as the reference
signal.Calculate the phase difference of the echo data of metal, water and hollow with the reference signal. Then the average phase difference is obtained as the input of the RBF neural network.
The ground penetrating radar feature data set used for training is divided into three categories, the metal target data, the water target data and the hollow target data. The characteristic data are marked with corresponding labels . Here, the subscript 1, 2, 3 represent water target, metal target and hollow target respectively.
The input of the RBF network is an array corresponding to average phase difference data samples. The output of the RBF network is a 1×3 array, from which the signal label is got and the training is completed. Then input the test data into the network, and calculate the error between the known classification results and the network classification results. Recognition successful rate can be obtained.
RECOGNITION AND CLASSIFICATION OF UNDERGROUND
TARGET MATERIAL BASED OF RBF
PROCESSING AND ANALYSIS OF SIMULATION RESULTS
Fig.2.(b) The signals after the direct wave is removed.
2021 IEEE 4th International Conference on Electronic Information and Communication Technology (ICEICT 2021)