## Slide 1
An Overview on Mission-Driven Networking Technologies in Data Link
Yuan Yongqiong1,2 *, Hu Junfeng1,2 , Zhang liang1,2
1Key Laboratory of Technology on Data link
2China Electronics Technology Group Corporation (CETC), 20th Institute, Xi’an, China
*E-mail: joannayuan2015@163.com
RELEVANT WORK
COMPARISON AND INTEGRATION DEVELOPMENT ANALYSIS OF MISSION DRIVEN NETWORKING TECHNOLOGIES
 | Advantages. | Limitations.
NPG-based networking | It can distinguish the way of using cyber source according to the characteristics of tasks. Based on the pre planning method, the integrated design of application message network structure access mode has high resource utilization efficiency The resource utilization based on pre planning and supplemented by dynamic slot allocation has low network management overhead | Limited resource dynamic adjustment, poor ability to adapt to dynamic changes and critical tasks Poor scalability
Information-based networking technology for a heterogeneous data link | Dual sensing (mission and channel) for traffic management and control Support planned and on-the-spot tasks Support heterogeneous multi-link Adapt to the contested environment | Limited awareness and understand of missions Medium network management overhead
Network slicing technology | Solve the network transmission requirements of application services with different bandwidth, delay and number of network user nodes. High utilization of network resources Adapt to the needs of business scenarios by providing end-to-end customized services | Poor ability to adapt to dynamic critical tasks High network management overhead No consideration against the contested environment
CONCLUSION
tactical data link network has gradually changed from mission-oriented single data link network to mission-driven multi-functional heterogeneous data link integrated network
Future heterogeneous data link networking can leverage the following techniques to enhance understanding of missions and flexibility in using network resources:
    Software defined networking
    Network slicing
    network function virtualization
    Intent-driven networking
Data link
  Link 16: TDMA , network participation group (NPG)
  TTNT: the Statistic Priority-based Multiple Access (SPMA) protocol
  DyNAMO: A two-tier dynamic communication model
  MINC: cross-network heterogeneous networking methods
5G
  network slice
others
  Application-centric
  Information-centric
  Mission capacity orient
REVIEW ON THE REPRESENTATIVE MISSION-DRIVEN NETWORKING SCHEMES
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
  NPG based Networking in Link16
NPG based Networking in Link16
  NPG is used to realize mission-oriented networking.
  NPG is also a means to describe the time slot.
  According to the mission characteristics and network capacity, each NPG determines: the network structure, Slot usage , Relay mode , etc
  Information based networking technology for heterogeneous data link
Information based networking technology for heterogeneous data link
  A two tier dynamic communication model is proposed to realize mission-oriented and environment-oriented networking.
Network slicing technology
  refers to the logical division and encapsulation of end-to-end network resources according to requirements of the service .
  Based on network resource virtualization and software componentization