## Slide 1
Research on Channel Equalization Algorithm in SC-FDE System
Cao Chenxi, Liu Guangzu, Zou Jun, Sun Linlin
Nanjing University of Science and Technology
Abstract
In this paper, zero-forcing equalization, minimum mean square error equalization and minimum mean square error adaptive equalization algorithms for SC-FDE systems are investigated, but the traditional LMS algorithms cannot meet the performance requirements of convergence speed and steady-state error at the same time because the step size factor is fixed. This paper investigates the variable step size LMS algorithm and proposes an improved variable step size LMS algorithm, which uses the non-linear relationship between the error factor and the error function to construct a correlation correction function, to regulate the error factor in a small range, and to further correct the step size factor through the change of the error factor.
SC-FDE system adopts the idea of OFDM system, at the transmitter side, the data firstly goes through the constellation map mapping, generally using QPSK and QAM mapping method, and then the data frame adds the protection interval, the protection interval usually uses the unique word (UW) . At the receiver side, firstly, the protection interval and data are distinguished, the protection interval is used for channel estimation, the data is converted to frequency domain signal by FFT, then channel equalization is performed and converted to time domain signal by IFFT and finally demodulated data is obtained by inverse constellation mapping. The block diagram of the SC-FDE system is shown below.
The specific steps to improve the variable-step LMS algorithm are summarized below.
System Principle of SC-FDE
Improved variable step size LMS adaptive equalization
Simulation Results
The figure gives the BER curves of different channel equalisation algorithms under the SUI-3 multipath channel.The ZF equalization algorithm is most affected by the multipath channel, with the BER plateau occurring at SNRs greater than 13dB, and the BER no longer increasing with SNR improves. At BER of , the performance of the improved variable step LMS equalization algorithm improves by 1dB over that of the variable step LMS equalization algorithm, by 1.5dB over that of the conventional LMS algorithm and by 2dB over that of the MMSE equalization algorithm.
The specific steps for improving the stepwise LMS algorithm are as follows:
Step 1: Initialise the tap coefficient vector, error vector
Step 2: When n=n+1
Calculate filter output :
Calculate errors :
Calculate error factor:
Update step:
Update filter tap coefficients: