## Slide 1
Design of Q-band Filter Based on Folded Step-Impedance Resonator
Shi Shan, Sun Linlin, Chu Ran, Liao Jia
Nanjing University of Science and Technology
Abstract
Theoretical analysis
Simulation and Analysis
Processing and Testing
Using HFSS electromagnetic simulation software to simulate the three-dimensional structure of the filter, Rogers 5880 was selected as the dielectric substrate, with a dielectric constant of 2.2, a loss angle tangent of 0.0009, and a thickness of 0.127mm, and its three-dimensional simulation model is shown in figure。
Based on the optimized results of the HFSS simulation, a physical filter was fabricated. The overall size of the filter is only 3.7mm x 3mm, and the performance curve was tested by a vector network analyser, and the comparison between the simulated and measured results is shown below.
In this paper, a miniaturized Q-band bandpass filter with high out-of-band rejection based on a stepped impedance resonator is designed. This filter championed a stepped-impedance resonator structure and is loaded with a stepped-impedance branch on the basic SIR, and the transmission zeros have been introduced through a special folded coupling feed line. Compared with the conventional SIR structure, it has more tuning parameters and a wider tuning range for resonant frequencies. A pair of transmission zeros are introduced simultaneously, which can enhance the rejection characteristics of the stop-band. The passband range of the filter is 43-46GHz, the in-band insertion loss is less than 3dB, the in-band return loss is larger than 15dB, and the out-of-band rejection is larger than 20dB in the frequency range of 35-43GHz and 46-55GHz.。
L1 | 0.75mm | W1 | 0.3mm | LS1 | 0.68mm
L2 | 0.375mm | W2 | 0.15mm | LS2 | 0.375mm
L3 | 0.6mm | W3 | 0.2mm | LS3 | 0.68mm
L4 | 0.34mm | W4 | 0.45mm | LS4 | 0.83mm
g1 | 0.1mm | g2 | 0.3mm | WS | 0.5mm
An SIR is a resonator consisting of two or more transmission lines with different characteristic impedances.
A T-shaped open-circuit branch is added to the center line of the resonator's one-half wavelength SIR that is symmetrical about the center. The loaded branch is effectively equivalent to forming a section of perturbation to separate the modes to form a passband.
In order to enhance the coupling between source and load while achieving the miniaturization requirement, a new folded coupled feeder structure is designed, and the topology is shown in figure.
After continuous scanning and optimization, the final parameter dimensions of the Q-band filter based on folded SIR with step-impedance branch loading are derived by considering the results of the influence of each parameter as shown in Table.
The actual measured S-parameter curve is basically similar to the simulation result curve.The measured in-band insertion loss is less than 4dB, the flatness is about ±1dB, the return loss is larger than 10dB, and the out-of-band rejection at 40GHz and 50GHz is less than -20dB.
Conclusion
Considering the test environment, dielectric substrate material, processing accuracy and assembly, this leads to poor grounding performance. Thus the actual tested in-band insertion loss and return loss is relatively poor. Although there is a certain degree of deterioration in certain result indicators of the actual measured results, the application based on folded step impedance resonator is basically completed.